## Slide 1
P0
P1
P2
P3
P4
P5
P6
P7
P8
PB15
PB14
PB13
PB12
PB10
PB11
PA5
PD12
PD13
3.3V Rail (250 mA supply Max)
GND Rail
VIN (3.6V - 5V)
ADC
DAC
UART 3
TX
UART 3
RX
SPI 2
SCLK
SPI 2
MISO
SPI 2
MOSI
SPI 2
SS
I2C 2
SDA
I2C 2
SCL
Servo 1
Servo 2
OpenMV Cam
LED1 – Red
LED2 – Green
LED3 – Blue
LED4 – IR
Micro SD Slot
SD < 2GB Max
SDHC < 32GB Max
SDXC < 2TB Max
Pin
Name
CPU
Name
Pin
Name
CPU
Name
Reset (Connect to GND to reset)
BOOT 0 (Connect to 3.3V for DFU mode)
ARM SWD Data (For Debugger access)
ARM SWD Clock (For Debugger access)
TIM4 CH1
TIM4 CH2
TM1
CH3N
TM1
CH2N
TM1
CH1N
TIM2
CH3
TIM2
CH4
TIM2
CH1
Peripherals / Timers
Peripherals / Timers
All pins are 5V tolerant1 with a 3.3V output
All pins can sink or source up to 25 mA2
1 P6 is not 5V tolerant in ADC or DAC mode
2 Up to 120mA in total between all pins
Max current used wo/ µSD card < 150 mA
Max current used w/ µSD card < 250 mA
By: Ibrahim Abdelkader & Kwabena W. Agyeman
https://.openmv.io
CAN2
RX
CAN2
TX