## Slide 1
P0
P1
P2
P3
P4
P5
P6
P7
P8
3.3V Rail (1A supply Max)
GND Rail
VIN (3.6V - 5V)
ADC
UART 1
TX
UART 1
RX
SPI 1
SCLK
SPI 1
MISO
SPI 1
MOSI
SPI 1
SS
I2C 1
SDA
I2C 1
SCL
OpenMV Cam RT1062
Micro SD Slot
SD < 2GB Max
SDHC < 32GB Max
SDXC < 2TB Max
Pin
Name
Pin
Name
Wakeup (Connect to ground to wakeup)
Reset (Connect to GND to reset)
Machine Module Peripherals / Timers
Machine Module Peripherals / Timers
All pins are 3.3V tolerant with a 3.3V output
All pins can sink or source up to 4 mA
By: Ibrahim Abdelkader & Kwabena W. Agyeman
https://openmv.io
CAN 0 RX
P9
PWM2 A0
CAN 0 TX
P10
ETH LED
ETH RXN
ETH RXP
ETH TXN
ETH TXP
ON/OFF
RAW
GND Rail
PWM1 X2
PWM1 X3
PWM2 B3
PWM2 B3
PWM2 B0
PWM1 A3
PWM1 B3
3.3V Rail
SBL
P13
P14
Reserved
Reserved
Reserved
Reserved
Frame Sync Input/Output
P11
On/Off (or Power Button):
* Pull low for 5 seconds to turn off when on
* Pull low for 1 second to turn on when off
Wake:
* Pull low to wakeup in deepsleep (not off).
RAW provides always-on unregulated (3.6V-5V) power in on/off or deepsleep modes.
Connect SBL to 3.3V to put the board into recovery mode to reflash the bootloader.
SW